## Slide 1: NIEM-UML-3 Specification Overview
Cory Casanave, Model Driven Solutions
September 2014 OMG Meeting
Austin, TX USA

## Slide 2: Current Status
The “Initial Submission to the UML Profile for NIEM-3 (NIEM-UML-3)” was delivered to the Object Management Group (OMG) on August 16th, 2014. Final submission due: Feb 23rd, 2015.
GITHUB Site
  Submission, machine readable files and design documents are on GITHIB site: https://github.com/NIEM/NIEM-UML/
  Contributors and reviewers are welcome
    Mail list: niem-uml@modeldriven.org
OMG Documents
  Submission: gov/2014-08-02
  Machine Readable Artifacts: on GITHUB
    Fully OMG conformant machine readable files have not yet been produced. Magicdraw and Eclipse files are available on GITHUB

## Slide 3: High level points
NIEM-UML-3 is a NIEM-3 update of the NIEM-UML specification (originally targeting NIEM 2.1) based on NIEM-XML-3
Good news: While there are substantial changes to NIEM-XML-3, the UML “Platform Independent Model” (PIM) profile and user models require minimal changes
Most NIEM-XML-3 changes are encompassed in:
  The automated “QVT” mappings from the PIM, through the PSM, to the NIEM artifacts
  The “MPD Profile” which supplies the metadata for a NIEM MPD. NIEM-3 has additional metadata capabilities
Today we will focus on these changes

## Slide 4: Major vs. Minor Release
NIEM 3.0 is a major release of the NIEM data model—containing updates to the NIEM Core as well as changes to several Domains.
A minor release involves limited changes to Domains

## Slide 5: How has NIEM evolved over the years?
Reference Schemas
MAJOR
NIEM 1.0
2006
1.0 Core
1.0 Domains
MAJOR
NIEM 2.0
2007
2.0 Core
2.0 Domains
MINOR
NIEM 2.1
2009
2.0 Core
2.1 Domains
MAJOR
NIEM 3.0
2013
3.0 Core
3.0 Domains

## Slide 6: NIEM 3.0 Inputs
Architectural Improvements
Resolved NIEM Configuration Control Tool (NCCT) Issues
Domain Content Updates & Additions
Content Harmonization
Content Related NCCT Issues

## Slide 7: NIEM 3.0 Normative Specifications
NIEM Naming and Design Rules V3.0
http://reference.niem.gov/niem/specification/naming-and-design-rules/3.0/
NIEM Model Pacakge Description Specification V3.0
http://reference.niem.gov/niem/specification/model-package-description/3.0/
NIEM Conformance Specification V3.0
http://reference.niem.gov/niem/specification/conformance/3.0/
NIEM Conformant Target Attribute Specification V3.0
http://reference.niem.gov/niem/specification/conformance-targets-attribute/3.0/
NIEM 3.0 was successfully launched on November 6, 2013. Various specifications serve as the “backbone” of the NIEM 3.0 technical architecture.

## Slide 8: Collaborative Innovation

## Slide 9: NIEM-UML Layered Architecture

## Slide 10: Platform Independent Model (PIM) Changes

## Slide 11: Unified Reference & Content
NIEM-UML-2
  UML “AggregationKind” (The symbol at the end of an association) corresponded with the “content” Vs. “Reference” distinction in NIEM-2
NIEM-UML-3
  No longer makes this distinction in the schema and uses “structures:ref” for reference – instances decide if and how to aggregate. UML aggregation may be used but has no meaning in NIEM-UML-3. Other possible interpretations can be considered.
  By default, aggregation kind of “none” is used
  Use of “Reference” suffix should be removed from models (may be automated by tools)
Has no impact on generated schema

## Slide 12: Unified content & reference elements In NIEM-XML
<j:ArrestInvolvedWeapon>
<nc:WeaponUser>
<nc:PersonBirthDate>
<nc:Date>1968-05-14</nc:Date>
</nc:PersonBirthDate>
<nc:PersonName>
<nc:PersonFullName>Mark Moe</nc:PersonFullName>
</nc:PersonName>
</nc:WeaponUser>
<nc:WeaponUsageText>Fired</nc:WeaponUsageText>
</j:ArrestInvolvedWeapon>
<j:ArrestInvolvedWeapon>
<nc:WeaponUser structures:ref="Person1"/>
<nc:WeaponUsageText>Fired</nc:WeaponUsageText>
</j:ArrestInvolvedWeapon>
<nc:Person structures:id="Person1">
<nc:PersonBirthDate>
<nc:Date>1968-05-14</nc:Date>
<nc:PersonName>
<nc:PersonFullName>Mark Moe</nc:PersonFullName>
</nc:PersonName>
</nc:PersonBirthDate>
</nc:Person>
CONTENT
REFERENCE

## Slide 13: NIEM-3 Augmentations
NIEM-2
  Augmentations augment a class by use of an property in a subclass
NIEM-3
  No subclass is required, augmentations augment a class by use of a substitution group head
NIEM-UML-3
  <<augments>> is used to augment a type. This generates the member of the substitution group.

## Slide 14: Augmentation Example
Restricted Augmentation of TelephoneNumber
<xsd:element name="TelephoneNumberAugmentation" nillable="false"
substitutionGroup="nc:TelephoneNumberAugmentationPoint " type="tns:TelephoneNumberAugmentationType">
.

## Slide 15: Augmentation Details
Use of <<AugmentationType>> is optional when using <<augments>>
An <<AugmentationType>> with no <<Augments>> can augment any type
  <<AugmentationApplication>> has been removed.
  You do not need to subclass the augmentation to use it – it will implicitly augment the base type and any subtypes
  Like the reference models, all NIEM-UML generated object types and association types will generate an augmentation point to allow for future expansion.

## Slide 16: Removed from NIEM-3
X
X
X
Only needed if there are other extensions

## Slide 17: NIEM-XML 3.0 Updated Augmentations
Augmentations are extensions without subclasses
Each object or association type contains an augmentation point element
Augmentation elements are substitutable for the augmentation point

## Slide 18: Local Vocabularies
Local vocabularies identify non-dictionary terminology: jargon, acronyms, slang
In NIEM-UML local vocabulary is defined as a stereotype of enumeration where each enumeration literal is a vocabulary term. The enumeration literal’s UML name corresponds with the domain specific abbreviation, the specification corresponds with the expansion of the abbreviation and the UML comment corresponds to the NIEM description. The NIEM sourceURI may also be set by applying the “Source” stereotype to the enumeration literal.
The above defines the abbreviation “CPU” (Expansion and description not shown in notation)

## Slide 19: NIEM-XML 3.0 Local vocabulary
Annotations in the schema identify non-dictionary terminology: jargon, acronyms, slang
Removes NDR 1.3 Table 9-1: Abbreviations
Used in Immigration namespace
<term:LocalTerm term="SEVIS"
literal="Student and Exchange Visitor Information
System"/>
<term:LocalTerm term="ICE"
literal="Immigration and Customs Enforcement"/>
<term:LocalTerm term="USCIS"
literal="United States Citizenship and Immigration
Services"/>
ICEEmployeeType
ICEOfficerType
SEVISPersonDependentAssociationType
ICEEmployee
ICEEmployeeAssistantUSAttorneyIndicator
ICEEmployeeAttorneyIndicator
ICEEmployeeAugmentationPoint
ICEEmployeeBadgeIdentification
ICEEmployeeK9Indicator
ICEEmployeePINIdentification
ICEEmployeePayGradeNumeric
ICEEmployeeTitleText

## Slide 20: Representation
NIEM-3 representation is used as the typeless head of a substitution group. This impacts the naming convention.
A representation property has no type.
NIEM-UML-3 supplies a stereotype, the naming convention may also be used.
Representation

## Slide 21: NIEM-UML-3 Common Profile

## Slide 22: NIEM-UML-3 PIM Profile

## Slide 23: Reference model changes
The NIEM reference models have undergone substantial changes.
NIEM-2 reference models may no longer be used
Tools may provide assistance in mapping NIEM-2 to NIEM-3 subset models, however this is not part of the NIEM-UML-3 specification
Not all mappings can be fully automated

## Slide 24: NIEM 3.0 Content Updates (changes from 2.1)
Domains
New Domain: Biometrics
Updates: Justice, CBRN, Immigration, Screening, Biometrics, International Trade, Maritime
Family Services (FS) changed its name to Children, Youth, & Family Services (CYFS)
Resolved issues in NIEM Configuration Control Tool (NCCT)
100+ NCCT issues backlogged after NIEM 2.0 and 2.1
~100 issues resolved since the NIEM 3.0 Kickoff in August
Significant object updates: LocationType (refactored), DocumentType, ContactInformation (types and associations), FacilityType, ItemType, BiometricType, Measures and MeasureType.
New code lists: HL7 (religion), GENC, Census-USCounty, occs-facility, DoL-soc (occupations), XCard (v-card XML representation)
Code list updates: FIPS (sunset lists), mmucc, nga-vdatum, ansi-d20
Harmonization: Justice & Biometrics, Immigration & Screening, CBRN & International Trade, Screening & Biometrics, Core & Biometrics

## Slide 25: NIEM 3.0 Technical Updates: abstract elements for codes
Code + Text with the same basic meaning
Release defines an abstract, typeless element for each
Code + Text are substituted for the base element

## Slide 26: MPD/IEPD Model Changes

## Slide 27: MPD Changes Overview
Where possible, no change was made to the 2.1 MPD profile and changes in NIEM accommodated via mapping
Much of the new metadata is captured in “UML Instance specifications”, not stereotype tags. This is due to the complexity of and linking between the metadata elements
Gone are: POC Type, Nature code, purpose code, ModelPackageDescriptionFile, ModelPackageDescriptionRelationship
  All moved to instance model
Examples will be provided in the next revision on GITHUB

## Slide 28: MPD Profile

## Slide 29: Profile points to class instances
Much of the MPD data is represented as UML instances (instances of classes). The profile elements reference these instances.

## Slide 30: Contact Information Classes

## Slide 31: MPD Artifact Classes

## Slide 32: MPD Validity Constraint Classes

## Slide 33: Other Specification Changes
All references to NIEM rules updated to NIEM-3
Structured English portion of specification removed as redundant with QVT
Overall improvement in documentation
Still to do
  Reference documentation generated from model
  High level documentation of revised QVT
  Finalize MPD section (not all changes reflected)
  Examples with complete metadata

## Slide 34: Automated changes
Changes in NIEM-3 that are taken care of by the NIEM-UML tooling

## Slide 35: NIEM 3.0 Technical Updates: Simplified structures
NIEM 2.0 | NIEM 3.0
structures:linkMetadata attribute | Replaced with structures:relationshipMetadata attribute
structures:sequenceID | Removed
structures:Augmentation element | Removed
structures:Metadata element | Removed
structures:ComplexObjectType | Replaced with structures:ObjectType and structures:AssociationType
structures Object and Association resources (for appinfo:Base) | Removed; extend from base types
structures:ReferenceType | Removed

## Slide 36: NIEM 3.0 Technical Updates: structures base types
Split ComplexObjectType into ObjectType, AssociationType
Added augmentation point element
Added structures:ref attribute
Renamed linkMetadata to relationshipMetadata
Added attribute wildcard for IC ISM, NTK namespaces

## Slide 37: NIEM-XML 3.0 Simplified annotations
NIEM 2.0 | NIEM 3.0
appinfo:ConformantIndicator | Schema: use attribute ct:conformanceTargets. Imports: use attribute appinfo:externalImportIndicator
appinfo:Base | Use the base types structures:ObjectType, structures:AssociationType.
appinfo:ReferenceTarget | Use the element's type attribute.
appinfo:AppliesTo | Augmentations: use the augmentation element's substitutionGroup attribute. Metadata: use attributes appinfo:appliesToTypes, appinfo:appliesToElements.
appinfo:ExternalAdapterTypeIndicator | Use attribute appinfo:externalAdapterTypeIndicator

## Slide 38: Simplified annotations

## Slide 39: NIEM 3.0 Technical Updates: simplified schemas

## Slide 40: Potential Improvements & Simplifications
The following have been suggested, the submission team is looking for feedback on the highest priorities
See: design/NIEM-3 Simplification.doc
Comments and priorities are being sought within 1 month

## Slide 41: Potential Simplification Summaries
General Information Models (OMG FTF Issue No: 18174)
  Have A PIM model type that brings together subsets and extensions
Augmentation Vs. multiple inheritance
  Make augmentation exactly like multiple inheritance (NIEM Issue)
Multiple subsets of the same type
  Allow multiple subsets of the same thing
Substitution groups as property holders
  Allow substitution groups “embedded” in class
Reducing the need for property holders
  Require property holders only for the edge cases
Usability of reference models
  Make them more “PIM LIKE”

## Slide 42: Potential Simplification Summaries
Aggregation commitment
  Have some interpretation for aggregation (Involve NTAC)
NIEM Association Types
  Represent reference models using association classes
Treatment of union types and substitution groups
  Allow unions of any class (e.g. entity)
Unnecessary Reified relationships (Association classes)
  Look for a way to have options for association realization (NTAC Issue)
Removal of explicit PSM profile
  Map directly from PIM to artifacts

## Slide 43: Summary of issues
Issue | Impact Estimate
General Information Models (OMG FTF Issue No: 18174) | 5
Subset Vs. extension schema | 4
Augmentation Vs. multiple inheritance | 2
Multiple subsets of the same type | 3
Substitution groups as property holders | 2
Entities Vs data elements | 1
Reducing the need for property holders | 2
Usability of reference models | 4
Aggregation commitment | 2
NIEM Association Types | 3
Treatment of union types and substitution groups | 3
Unnecessary Reified relationships (Association classes) | Unknown
Removal of explicit PSM profile | 3

## Slide 44: Questions and Comments